## Slide 1
Presented by:
VIJAY ANAND V (192413029) ABDUL AZEEZ S (192413012)
HARI PRASAD L S (192413023)
Capstone project presentation
Vision-Based Driver Drowsiness Detection Using Python and MediaPipe with ESP32-CAM Controlled Relay, Motor, Buzzer and TFT Display System
EEA-3101 ELECTRIC VEHICLE TECHNOLOGY FOR INDUSTRIAL INNOVATION
Guided By :
DR. S. Padmakala
SAVEETHA INSTITUTE OF MEDICAL AND TECHNICAL SCIENCES

## Slide 2
01 / Challenge
Problem Statement
Driver Drowsiness Causes Accidents
Drowsy driving is responsible for thousands of fatalities annually, making it a critical road safety concern worldwide.
Lack of Real-Time Monitoring
Traditional vehicles lack intelligent systems to continuously monitor driver alertness and intervene before accidents occur.
Need for AI-Based Safety
Advanced AI-powered solutions are essential to detect early signs of drowsiness and prevent potential disasters.
100,000+
Annual drowsy driving crashes reported
6,500
Fatalities caused by drowsy driving yearly
$12.5B
Annual economic losses from fatigue-related accidents

## Slide 3
02 / Goals
Project Objective
Real-Time Emotion Detection
Continuously monitor and analyze driver facial expressions to detect emotional states using AI-powered computer vision algorithms.
Drowsiness Identification
Accurately identify sleeping or drowsy states by analyzing eye closure patterns, head position, and facial landmark movements.
Audio Alert System
Immediately alert the driver using a buzzer alarm when drowsiness is detected, providing instant warning to regain attention.
Automatic Safety Stop
Automatically stop the motor/vehicle when critical drowsiness is detected, preventing potential accidents through hardware control.
Visual Feedback Display
Show detected emotion status on TFT screen for real-time monitoring and system diagnostics

## Slide 4
03 / Design
System Architecture
Complete data flow from image capture to safety action
Camera
Captures video feed
AI Processing
MediaPipe Analysis
Serial Comm
Data transmission
ESP32
Central controller
TFT Display
Shows emotion status
Buzzer
Audio alert
Relay
Motor control
Motor Stop
Vehicle safety shutdown when drowsiness detected

## Slide 5
04 / Stack
Software Technologies
Python
Primary programming language for AI model development, data processing, and system integration with extensive library support.
OpenCV
Computer vision library for real-time image processing, video capture, and preprocessing facial data before AI analysis.
MediaPipe
Google's ML solution for face landmark detection with 468 facial points, enabling precise emotion and drowsiness analysis.
PySerial
Python library enabling serial communication between AI processing unit and ESP32 microcontroller for data transmission.
Arduino IDE
Development environment for programming ESP32 firmware, controlling hardware components, and managing I/O operations

## Slide 6
05 / Components
Hardware Components
ESP32 Dev Board
Dual-core microcontroller with Wi-Fi/Bluetooth for central control and processing
1.8" TFT LCD
ST7735 color display for real-time emotion status visualization and feedback
Relay Module
Electromechanical switch for controlling high-power motor circuits safely
Buzzer
Piezoelectric audio alarm for immediate drowsiness alerts to the driver
DC Motor
Represents vehicle propulsion system controlled via relay for safety stop
Breadboard & Wires
Prototyping platform and connections for circuit assembly and testing
System Integration: All components work together to create a complete drowsiness detection and safety response system

## Slide 7
06 / Process
Working Principle
1
Face Capture
Webcam continuously captures driver's face in real-time at 30 FPS for analysis
2
Landmark Detection
MediaPipe identifies 468 facial landmarks including eyes, mouth, and head position
3
Emotion Classification
AI algorithm analyzes landmarks to classify emotions: NORMAL, DROWSY, or SLEEPING
4
Data Transmission
Detected emotion status sent to ESP32 via serial communication (UART)
5
Safety Action
If SLEEPING detected: buzzer alerts, relay stops motor, TFT displays warning
Facial Landmarks
Eyes: 12 points per eye for blink detection
Mouth: 20 points for yawning detection
Head: Orientation and nodding analysis
Eyebrows: Expression and fatigue indicators
468
Total facial landmarks detected by MediaPipe for comprehensive analysis

## Slide 8
07 / Safety
Safety Mechanism
IF emotion = SLEEPING
Buzzer Activates
Immediate audio alarm to wake driver
Relay Cuts Power
Motor power disconnected for safety
TFT Shows Emoji
Sleeping emoji displayed on screen
CRITICAL SAFETY MODE
IF emotion = NORMAL
Motor Runs Normally
Vehicle continues operation without interruption
NORMAL OPERATION MODE
Decision Logic: System continuously monitors driver state and instantly switches between normal operation and safety mode based on AI analysis

## Slide 9
09 / Summary
Conclusion & Future Scope
Conclusion
AI Improves Driver Safety
Machine learning algorithms accurately detect drowsiness, preventing potential accidents before they occur
Automation Prevents Accidents
Automatic motor stop and alert systems provide immediate safety intervention without human delay
AI & IoT Integration Success
Seamless combination of computer vision, embedded systems, and hardware control demonstrates practical AI application
Future Scope
ESP32-CAM Integration
Built-in camera module for standalone operation without external computer
Cloud Monitoring
Remote data logging and fleet management through IoT cloud platforms
Mobile App Alerts
Real-time notifications to fleet managers and emergency contacts
Real Vehicle Integration
Direct connection to vehicle braking and steering systems for enhanced safety
Technology for Safer Roads